## Slide 1: ECE510 Project Proposal
Rohit Kulkarni Anuja Vaidya

## Slide 2: Modules in Design
Clkgen_driver
Instr_decode
Instr_exec
Memory_pdp

## Slide 3: IFD Unit
Fetches instruction
Decodes fetched instruction
Supports decoding of
  6 memory reference instructions
    Opcode 0 to 5
  22 microinstructions
    Opcode 7 : Group 1 and Group 2

## Slide 4: IFD FSM

## Slide 5: EXEC Unit
Executes instruction decoded by IFD unit.
Accesses memory if instruction among opcodes 0 to 5.
Reads operand from memory
Writes result into memory
Stalls IFD unit until current instruction completes execution

## Slide 6: EXEC Unit FSM

## Slide 7: Verification Strategy
Unit Level Testbenches for
  IFD Unit
  EXEC Unit
Full chip validation for entire design

## Slide 8: Unit Level TB: IFD

## Slide 9: Unit Level TB: IFD
Components needed:
  Instr_decode (DUT)
  Exec_BFM
  Memory_BFM
  Clk_gen_driver
  Checker

## Slide 10: Validation Strategy for IFD
Stimulus:
  IFU_RD_DATA from MEMORY_BFM
  STALL from EXEC_BFM
  PC_VALUE from EXEC_BFM
  RESET_N from CLK_GEN
Checks to perform:
  Check if opcode sent to EXEC is correctly decoded
  Check if address sent to EXEC is correctly decoded
  When STALL is asserted, IFD should not fetch the next instruction and no new requests sent to EXEC unit
  If reset_n asserted at any point, then all outputs are cleared within 1 clock cycle
  On asserting reset, next instruction should be fetched from o200
  If current state = STALL and PC = 0200, then next state = DONE
  No instructions are fetched after going into DONE state
Coverage:
  State coverage, Arc coverage, Path Coverage

## Slide 11: Unit Level TB: EXEC

## Slide 12: Unit Level TB: EXEC
Components needed:
  Instr_exec (DUT)
  Instr_decode_BFM
  Memory_BFM
  Clk_gen_driver
  Checker

## Slide 13: Validation Strategy for EXEC
Stimulus:
  PDP_OPCODE from INSTR_DECODE_BFM
  EXEC_RD_DATA from MEMORY_BFM
  RESET_N from CLK_GEN
Checks to perform:
  Check if result is corrected correctly
  Check if result computed is written to memory for certain instructions
  Check if LINK bit is correctly computed
  Check if STALL is asserted after beginning to execute each opcode
  Check if STALL is deasserted after completion of execution of each opcode
  Check if illegal opcodes are executed as NOP
Coverage:
State coverage, Arc coverage, Path Coverage

## Slide 14: Full chip TB

## Slide 15: Validation Strategy for Full-Chip
Stimulus: Assembly code loaded in memory
Stimulus should write result to memory after each operation so that checker checks the result
Checks to perform:
  Tap memory interface with IFD/EXEC for
  Instruction fetched
  Operand fetched
Compute Golden Result and check if Actual Result matches Golden Result

## Slide 16: Questions?